## Slide 1
HARDWARE-SOFTWARE CO-DESIGN
PARISCV v2: Automated Custom-Instruction Discovery and its execution , Speedup of mac operations
Closing the loop from plain C source code to real OpenHW RISC-V silicon RTL acceleration
3.99× ≈ 4.0×
RTL Speedup on TinyML INT8 SIMD (CV32E40X Coprocessor)
5-Stage Flow
Push-button automated C-to-Silicon toolchain (<15s runtime)
Notes: Welcome everyone. Today I'm presenting PARISCV v2, an end-to-end framework that takes unmodified C code, discovers custom instruction opportunities, and synthesizes, compiles, and verifies them on cycle-accurate OpenHW RISC-V silicon RTL in Verilator. We achieved a 4x hardware speedup on TinyML workloads by overcoming the coprocessor interface latency bottleneck.

## Slide 2
PROBLEM CONTEXT
The Offload Dilemma: Why Naive Coprocessors Fail
CV-X-IF 2-Cycle Synchronous Handshake
1. Cycle 1 (Issue Phase): Core decodes opcode 0x0b, drives xif_issue_if.issue_valid, and routes rs1, rs2, rs3 to coprocessor.
2. Cycle 2 (Result Phase): Coprocessor computes arithmetic and asserts xif_result_if.result_valid. Core commits writeback to rd.
Result: Any offload over CV-X-IF incurs an unavoidable 2-cycle interface penalty (TXIF = 2 cycles).
The Scalar MAC (pg.mac) Failure
In standard software, scalar Multiply-Accumulate takes 2 cycles (1 cycle MUL + 1 cycle ADD).
Speedup = T_SW / T_XIF = 2 cycles / 2 cycles = 1.00× (0.0% Speedup)
Key Takeaways & Offload Rules:
• 2-instruction scalar fusion across CV-X-IF can NEVER win. • A fused sequence must take ≥ 3 cycles in software to justify offload. • We must exploit SIMD data parallelism to overcome interface latency.
Notes: Here is the core problem: CV-X-IF is a synchronous coprocessor interface that takes 2 clock cycles minimum. When previous works tried offloading scalar multiply-accumulate (pg.mac), software took 2 cycles and hardware took 2 cycles. The result was exactly 0% speedup. This established our microarchitectural rule: scalar fusion fails on coprocessors; we need SIMD parallelism.

## Slide 3
HARDWARE ARCHITECTURE
The pg.sdot4 Breakthrough: 4-Lane INT8 SIMD on CV32E40X
Packed 8-Bit Dot-Product with 32-Bit Accumulation
• Instruction: pg.sdot4 rd, rs1, rs2, rs3 (Custom R4-Type, Opcode 0x0b) • Datapath: Four parallel 8x8 signed multipliers + adder tree + 32-bit accumulator
Mathematical Definition: rd ← rs3 + Σ (rs1[8k+7 : 8k] × rs2[8k+7 : 8k]) for k = 0,1,2,3..
Why we get the speedup? : • Computes 4 MAC operations in the same 2-cycle CV-X-IF handshake. • Effective Throughput: 0.5 cycles per MAC (vs 2.0 cycles in software)!
Concrete Computation Example
Given Accumulator rs3 = 100: • rs1 = [2, -1, 3, 4] (Hex: 0x02FF0304) • rs2 = [1, 5,-2, 3] (Hex: 0x0105FE03)
Hardware Execution (2 cycles): rd = 100 + (2×1) + (-1×5) + (3×-2) + (4×3) rd = 100 + 2 - 5 - 6 + 12 = 103
Software equivalent requires: • 4 byte loads + 4 sign-extensions + 4 multiplies + 4 adds (≈ 16 cycles) • Hardware replaces 14 instructions with a single 2-cycle instruction.
Notes: To break the latency bottleneck, we designed pg.sdot4. It packs four 8-bit signed integers into standard 32-bit registers. In the exact same 2-cycle CV-X-IF handshake, four 8x8 multipliers execute in parallel, sum through an adder tree, and accumulate into rs3. This reduces cost from 2.0 cycles per MAC to 0.5 cycles per MAC, delivering a 4x theoretical speedup.

## Slide 4
HARDWARE ARCHITECTURE
Native In-Pipeline ALU Instructions on CV32E40P
1. pg.rol (Rotate Left)
Target: Nettle SHA-256 & MD5 Latency: 1 cycle (In-pipeline)
Operation: rd = (rs1 << rs2) | (rs1 >> (32 - rs2)) Impact: • Replaces 4 instructions (sll, srl, sub, or) with 1 cycle ALU op. • 14.3% cycle reduction on SHA-256 (4,468 cycles saved). • 4.2% cycle reduction on MD5 (2,054 cycles saved).
2. pg.idx (Table Index)
Target: CRC-32 Checksum Latency: 1 cycle (In-pipeline)
Operation: rd = rs2 + ((rs1 & 0xFF) << 2) Impact: • Fuses byte masking (andi 0xFF), word shift (slli 2), and base address addition (add). • 10.7% cycle reduction on CRC-32 (2,124 cycles saved). • Replaces table address calculation sequences.
3. pg.sha (Shift-Add)
Target: EDN Digital Filter Latency: 1 cycle (In-pipeline)
Operation: rd = (rs1 >>> 15) + rs2 Impact: • Fuses arithmetic right shift (srai 15) and accumulator addition (add). • 4.1% cycle reduction on EDN (1,749 cycles saved). • Demonstrates in-pipeline ALU fusion for digital signal processing.
Notes: On CV32E40P, which lacks a coprocessor interface, we integrated custom instructions directly into the core's ALU and decoder. Because these execute inside the pipeline with 1-cycle latency and zero handshake overhead, even simple operations like rotate left, table indexing, and shift-add achieve solid 4% to 14% real cycle savings.

## Slide 5
PUSH-BUTTON AUTOMATION
The 5-Stage Automated C-to-Silicon Toolchain
Stage 1
Idiom Detector
tools/idiom_detector.py
• Scans plain C code • AST & regex matching • Identifies sdot4, rol, idx loops • Binds to target core
Stage 2
Source Rewriter
tools/c_rewriter.py
• Puts intrinsics header • Replaces C loops with __builtin_pg_*() • Emits clean standalone <file>_accel.c
Stage 3 & 4
Dual Firmware Builder
tools/firmware_builder.py
• Bare-metal GCC toolchain • -Os -nostdlib -march • Links link_rtl.ld • Emits baseline & accel .hex
Stage 5
Verilator RTL Runner
tools/verilator_runner.py
• Executes testbench_verilator • Relative +firmware= paths • Parses rdcycle registers • Validates MMIO exit (0x0)
Stage 5b
Silicon Report & Verify
Bit-Exact Matching
• Checksum check (result=1) • Computes verified speedup • Formats CLI report • Total time: <15 seconds!
Single CLI Command Execution: python3 pariscv_flow.py --auto-accelerate bench_mac.c --core cv32e40x
Notes: This slide shows the main systems contribution: pariscv_flow.py. It completely eliminates manual assembly coding. A developer gives the tool plain C code. In stage 1 and 2, it detects vector and crypto idioms and rewrites the source with hardware intrinsics. In stages 3, 4, and 5, it cross-compiles both baseline and accelerated binaries, runs them on Verilator silicon RTL, and checks bit-exact mathematical output, all in under 15 seconds.

## Slide 6
EXPERIMENTAL RESULTS
Verified Silicon RTL Performance Improvements
Instruction | Evaluation Benchmark | Baseline Cyc | Accel Cyc | Saved | Reduction | HW Speedup
pg.sdot4 | MAC.C (1024-elem) | 13,323 | 3,339 | 9,984 | 74.9% | 3.99× ≈ 4.0×
pg.rol | Nettle SHA-256 | 31,240 | 26,772 | 4,468 | 14.3% | 1.17×
pg.idx | CRC-32 Checksum | 19,842 | 17,718 | 2,124 | 10.7% | 1.12×
pg.rol | MD5 Hash Algorithm | 48,910 | 46,856 | 2,054 | 4.2% | 1.04×
pg.sha | EDN | 42,650 | 40,901 | 1,749 | 4.1% | 1.04×
pg.mac | Scalar MAC (1024-elem) | 13,323 | 13,323 | 0 | 0.0% | 1.00× (Control)
100% Bit-Exact Verification: All hardware runs passed mathematical checksums (result == 1) with clean EXIT SUCCESS (0).
Notes: Here are the silicon RTL results on Verilator. pg.sdot4 achieved a 74.9% cycle reduction, delivering a 4.0x hardware speedup. In-pipeline instructions on CV32E40P achieved 4% to 14% speedup. The bottom row highlights our negative control: scalar pg.mac confirms the 0.0% speedup predicted by the 2-cycle offload model.

## Slide 7
MICROARCHITECTURAL ANALYSIS
Architectural Stall Decomposition (20 Embench Workloads)
Where Do The Cycles Go?
Analysis across 20 Embench workloads reveals why custom instructions only help certain kernels:
1. Control-Flow Dominance: • Kernels like primecount (31% branch) and tarfind (35% branch) are branch-bound. • Arithmetic ISE cannot accelerate control flow.
2. Free Cycles in Alignment: • Branch target misalignment alone costs 2.2% to 8.4% of total cycles. • On edn, alignment fixes save 4,465 cycles—more than enabling bitmanip (Zbb)
Benchmark | Baseline | Comp% | Br% | Candidate | Gain
bench_mac.c | 13,323 | 76.2% | 12.1% | pg.sdot4 | 67.6%
nettle-sha256 | 31,240 | 79.4% | 8.2% | pg.rol | 14.3%
crc32 | 19,842 | 71.5% | 14.2% | pg.idx | 10.7%
md5 | 48,910 | 82.1% | 6.4% | pg.rol | 4.2%
edn | 42,650 | 74.8% | 11.9% | pg.sha | 4.1%
matmult-int | 124,500 | 73.1% | 14.5% | pg.mac | 0.0%
primecount | 162,340 | 52.4% | 31.0% | None | 0.0%
tarfind | 58,210 | 49.8% | 35.1% | None | 0.0%
wikisort | 215,400 | 51.2% | 33.2% | None | 0.0%
statemate | 38,400 | 58.1% | 28.4% | None | 0.0%
Notes: We classified all 20 Embench benchmarks to understand architectural limits. On workloads with high compute ratios like TinyML, SHA-256, and CRC32, custom instructions deliver high speedups. However, on workloads like primecount and wikisort, control flow takes over 30% of cycles, showing that custom arithmetic cannot help without control-flow hardware support.